# Pick and Place

Pick and Place output

The generated files contain the following information for each component used in the design:
- Designator
- Footprint
- Location
- Layer (TB Top/Bottom)
- Rotation
- Comment

The location information is expressed in three ways, corresponding to the three methods by which a component footprint's reference point can be specified in the source PCB library:
- Mid X , Mid Y - coordinates for the component's center point
- Ref X , Ref Y - coordinates for the component's user-defined reference point
- Pad X , Pad Y - coordinates for Pad 1 of the component.

# Fiducial Marks

You need 3 of them and they need to be placed in an L shape. ( that means : at three corners of the board )
The one in the corner of the L has a different shape than the others.

you typically put the corner one on coordinates o.o
the square one is centered at 0:0
the others sit at 0,x and y,0

You need these on top and bottom lyer ( if you have parts on both sides )
You need to make 2 pcb footprints. one with a square SMD pad and one with a round SMD pad. They don;t neeed to be large. i use 20 mil diameter pads. The soldermask peelback needs to be 15 mils so the robot gets a good contrasted view. You cannot have ANYTHING in a circle 20 mils around the fiducial.. no copper, no parts, no text .

Global Fiducials	Local Fiducials
Fiducial marks used to locate the position of all features on an individual printed circuit board. When multiple boards are processed as a panel, the global fiducials may also be referred to as panel fiducials if used to locate the circuits from the panel datum.	Fiducial marks used to locate the position of an individual component that may require more precise location, such as a .020” pitch QFP

The minimum diameter of the fiducial mark should be 1mm (0.040 in). The maximum diameter of the fiducial should be 3mm (0.120 in). Fiducial marks on the same PCB should not vary in size by more than 25 microns (0.001 in).

# Library methodolgy

schematic libraries / *.SchLib	Absolutely required library type / Contains schematic components that are graphically and electrically represented by a schematic symbol. / Speciﬁ c parametric information (such as part number and component values), are typically added to each component and can be accessed during the generation of the bill of materials (BOM). / One or more PCB footprints, as well as optional SPICE simulation (*.MDL or *.CKT ﬁ les) and signal integrity (SI) (*.IBIS) models, are linked to the schematic / component.
PCB libraries / *.PcbLib	Absolutely required library type / Contains PCB footprints that represent the physical pad arrangement and other mechanical attributes of the component. / Optionally, solid model 3D information in the STEP format (*.STEP ﬁles) can be added to the footprint to represent the component’s physical shape in 3D mode.
integrated library / *.IntLib	A single read-only ﬁle representing an entire library of many components / All linkages of the component to symbols, footprints, simulation, and SI models are permanent, so library-related design errors are minimized compared to just working with the separate essential library ﬁles. / The resulting single ﬁle representing an entire library is easy to distribute and manage.
database library / *.DBLib	Components are managed as a set of database rows and columns. / Each row in the database table begins with a key lookup identiﬁer, which is typically a manufacturer part number or an internal corporate part number. / The remaining column information deﬁ nes each row as the component’s symbol, / footprint, simulation model, SI model, and any number of additional parametric attributes. / The main advantage of a database library is the access to a component’s parametric data from a common set of part information within an organization. / This enables you to create a BOM with information accurately reﬂecting that used by the purchasing and accounting departments. / Each unique component ID is a single orderable item from one or more suppliers. / Database libraries access the required symbols and footprints from the essential schematic (*.SchLib) and PCB (*.PcbLib) libraries respectively. / The database library can be advanced one step further to an SVN database library (*.SVNDBLib) where the individual symbols and footprints can be managed under version control.
component library / *.CmpLib	Is used to associate all aspects (schematic capture, 2D/3D PCB layout, simulation, signal integrity) of a given component as an individual, revisioned item in a centrally accessible Vault. / The design component is separate from the manufacturer or supplier data. Such information is not deﬁ ned as part of the component, but instead as a separate Vault item (a Part Choice List item) used to map a design component to one or more manufacturer parts. In turn, this can be mapped to one or more supplier parts, providing real-time supply chain information such as pricing and quantity available from each supplier. / In addition to real-time links to the supply chain, the vault enables strict control over authorized or approved components, item updates and revisions, and component lifecycle status.