https://en.wikipedia.org/wiki/List_of_integrated_circuit_packaging_types

Flat packages
Small outline packages
Chip-Scale packages
Ball grid array
Transistor, diode, small pin count IC packages

# SOIC = Small Outline Integrated Circuit
https://en.wikipedia.org/wiki/Small_Outline_Integrated_Circuit

Narrow SOIC (JEDEC)
Wide SOIC	The difference is mainly related to the parameters WB and WL
MSOIC	SOIC variant, available only for 8-pins and 10-pins ICs, is the mini-SOIC, also called micro-SOIC. This case is much smaller with a pitch of only 0.5mm.
SOJ	is a version of SOIC with J-type leads instead of gull-wing leads.
SOP	a family of smaller form factors , with pin spacings less than 1.27 mm / Plastic small outline package (PSOP) / Thin small outline package (TSOP) / Thin-shrink small outline package (TSSOP)

# SOIC-8-N

# SOIC-16-W

# TSSOP-24
http://www.analog.com/en/design-center/packaging-quality-symbols-footprints/package-index/sop-small-outline-package/tssop-thin-1_2mm.html

# QFP = Quad Flat Package
TQFP = thin quad flat pack	T is for thin(er, 1.0 mm)
LQFP = Low Profile Quad Flat Package	L is for Low-profile (1.4 mm)

## LQFP-32

## LQFP-64

# SOT = Small Outline Transistor

## SOT23-5

# DO = Diode

DO-214AA, also known as SMB,is the middle size.
DO-214AB, also known as SMC,is the largest size.
DO-214AC, also known as SMA,is the smallest size.