# Pick and Place

Pick and Place output

The generated files contain the following information for each component used in the design:
- Designator
- Footprint
- Location
- Layer (TB Top/Bottom)
- Rotation
- Comment

The location information is expressed in three ways, corresponding to the three methods by which a component footprint's reference point can be specified in the source PCB library:
- Mid X , Mid Y - coordinates for the component's center point
- Ref X , Ref Y - coordinates for the component's user-defined reference point
- Pad X , Pad Y - coordinates for Pad 1 of the component.

# Fiducial Marks

You need 3 of them and they need to be placed in an L shape. ( that means : at three corners of the board )
The one in the corner of the L has a different shape than the others.

you typically put the corner one on coordinates o.o
the square one is centered at 0:0
the others sit at 0,x and y,0

You need these on top and bottom lyer ( if you have parts on both sides )
You need to make 2 pcb footprints. one with a square SMD pad and one with a round SMD pad. They don;t neeed to be large. i use 20 mil diameter pads. The soldermask peelback needs to be 15 mils so the robot gets a good contrasted view. You cannot have ANYTHING in a circle 20 mils around the fiducial.. no copper, no parts, no text .

Global Fiducials	Local Fiducials
Fiducial marks used to locate the position of all features on an individual printed circuit board. When multiple boards are processed as a panel, the global fiducials may also be referred to as panel fiducials if used to locate the circuits from the panel datum.	Fiducial marks used to locate the position of an individual component that may require more precise location, such as a .020” pitch QFP

The minimum diameter of the fiducial mark should be 1mm (0.040 in). The maximum diameter of the fiducial should be 3mm (0.120 in). Fiducial marks on the same PCB should not vary in size by more than 25 microns (0.001 in).